# Text boxes

Gradus is a member of NBS Plus, providing a comprehensive library of pre-written specifications supported by guidance notes. The NBS specification for Gradus Grip is shown below, plus a detailed Gradus specification and profile description to ensure the correct specification is maintained. For further information on NBS contact NBS Services on 0191 232 9594.

NBS Specification

L30 Stairs/ ladders/ walkways/ handrails/ balustrades

10 WOOD STAIRS

L30 Stairs/ ladders/ walkways/ handrails/ balustrades

590 APPLIED STAIR NOSINGS

M50 Rubber/ plastics/ cork/ lino/ carpet tiling/ sheeting

75 STAIR NOSINGS AND TRIMS

M50 Rubber/ plastics/ cork/ lino/ carpet tiling/ sheeting

750 STAIR NOSINGS AND TRIMS

M51 Edge fixed carpeting

550 STAIR NOSINGS AND TRIMS

Manufacturer: Gradus Accessories, Park Green, Macclesfield, Cheshire, SK11 7LZ.

Tel: 01625 428922 Fax: 01625 433939

Website: www.gradusworld.com   Email: sales@gradusworld.com

Reference: Gradus Grip

Colour: White

Tube Size: 290ml

Open time (maximum, at 23˚C and 50% RH): Ten minutes.

Curing time (foot traffic): 	Absorbent surfaces: Approximately one hour - as per manufacturer's instructions.

Non-absorbent surfaces: Approximately two hours - as per manufacturer's instructions.

Gradus Detailed Specification

Manufacturer: Gradus Accessories, Park Green, Macclesfield, Cheshire, SK11 7LZ.

Tel: 01625 428922 Fax: 01625 433939

Website: www.gradusworld.com   Email: sales@gradusworld.com

Reference: Gradus Grip

Colour: White

Tube Size: 290ml

Open time (maximum, at 23˚C and 50% RH): Ten minutes.

Curing time (foot traffic): 	Absorbent surfaces: Approximately one hour - as per manufacturer's instructions.

Non-absorbent surfaces: Approximately two hours - as per manufacturer's instructions.

Warranty: 10 year on both the Gradus stair edging and Gradus Grip.  Full Warranty details available on request.

Installation Instructions: Consult with Gradus Techincal Support or visit http://www.gradusworld.com/gradus-grip for full installation advice.

Description

Gradus Grip

A solvent free, rapid curing flexible adhesive with excellent gap filling properties which is suitable for bonding Gradus stair edgings to most solid surfaces in internal and external environments. When fixing to suitable solid substrates mechanical fixings are not required.

Data Sheet:   February 2016

Gradus Accessories, Park Green, Macclesfield, Cheshire SK11 7LZ England UK  Tel: 01625 428922  Fax: 01625 433949

www.gradusworld.com

# NBS & Gradus Specifications

# Gradus Grip