# Text boxes

Installation Guidelines

# Accessories

SCSM471 Cover Strip

Gradus Accessories, Park Green, Macclesfield, Cheshire SK11 7LZ England UK  Tel: 01625 428922  Fax: 01625 433949

www.gradusworld.com

Data Sheet:   (sheet 1 of 1)   05/06/15

- It should be ensured that all surfaces to which the profile is to be fixed are dry, flat and free from any contaminants.

- Cut the profile to the size required.

- Place the profile into position and through the pre-drilled holes, mark the substrate.

- Drill the marked substrate using a 5mm drill bit and once drilled insert the appropriate sized plug.  (5mm = yellow plug).

- *On timber subfloors, fix using No4 wood screws.

- Secure in place using a No4 fixing screw.

- If any further information is required, please do not hesitate to contact Gradus Technical Services on (+44)1625 428922 or fax on (+44)1625 425226