# Text boxes

Gradus is a member of NBS Plus, providing a comprehensive library of pre-written specifications supported by guidance notes. The NBS specification for Wall Street is shown below, plus a detailed Gradus specification and profile description to ensure the correct specification is maintained. For further information on NBS contact NBS Services on 0191 232 9594.

NBS Specification

M50 RUBBER/PLASTICS/CORK/LINO/CARPET TILING/SHEETING

130 CARPET TILE; 170 CARPETING:

Manufacturer: Gradus Carpets, Park Green, Macclesfield, Cheshire, SK11 7LZ.

Tel: 01625 859000 Fax: 01625 850352

Website: www.gradusworld.com   Email: sales@gradusworld.com

Reference: Gradus Wall Street

Type: Tufted Structured Loop Pile Carpet Tile

Gradus Detailed Specification

Manufacturer: Gradus Carpets, Park Green, Macclesfield, Cheshire, SK11 7LZ.

Tel: 01625 859000 Fax: 01625 850352

Website: www.gradusworld.com   Email: sales@gradusworld.com

Reference: Gradus Wall Street

Construction: Tufted Structured Loop Pile

Surface Yarn: 100% Aquafil Econyl Solution Dyed Nylon

Dimensions/backing:  500mm x 500mm Bitumen Backed

Total Carpet Thickness: 7mm

Primary backing: Synthetic Non-Woven

Colours: Available in 12 colourways

Warranties: 10 year wear warranty and 10 year anti-static warranty (Full details on request)

Consult with Gradus Carpets for technical literature and to obtain samples.

Gradus Carpets can also provide a design and specification advisory service and it is recommended that they are consulted early in the design process.

Installation Instructions;

500mm x 500mm Carpet Tiles, recommended adhesive.  F. Ball & Co.  01538 361633.  Product F41

All carpet should be laid in accordance with BS5325:2001 installation of textile floorcovering.

For further installation advice, please contact Gradus Technical Services 01625 428922

Description

Wall Street

Wall Street features an attractive plain textured design in loop pile construction.  Wall Street can be used alone or can coordinate with Wall Street Stripes to create interesting and unique floor schemes.  Wall Street is suitable for a wide variety of environments including commercial, education and healthcare.

Data Sheet:   (sheet 1 of 1)   July 2012

# Floorcoverings

# NBS & Gradus Specifications

Gradus Carpets, Park Green, Macclesfield, Cheshire SK11 7LZ England UK  Tel: 01625 428922  Fax: 01625 433949

www.gradusworld.com

Wall Street