# Text boxes

- It should be ensured that all surfaces to which the profile is to be fixed are dry, flat and free from any contaminants.

- Cut the BU200 to the size required.

- Apply a proprietary contact adhesive to the underside of the BU200 and the floor.

- Allow the adhesive to become touch dry.

- Apply bevelled underlay to the floor and apply firm pressure to ensure full contact with the substrate.

- Apply floorcovering over the installed BU200.

If any further information is required, please do not hesitate to contact Gradus Technical Services on (+44)1625 428922 or fax on (+44)1625 425226

Data Sheet:   (sheet 1 of 1)   28/02/08

# Accessories

Installation Guidelines

Gradus Accessories, Park Green, Macclesfield, Cheshire SK11 7LZ England UK  Tel: 01625 428922  Fax: 01625 433949

www.gradusworld.com

BU 200 Bevelled Underlay