# Text boxes

- It should be ensured that all surfaces to which the profile is to be fixed are dry, flat and free from any contaminants.

- Cut the profile to the size required.

- Place the base into position and through the pre-drilled holes, mark the substrate.

- Drill the marked substrate using a 6mm drill bit and once drilled insert the appropriate sized plug.  (6mm = red plug).

- Apply a bead of proprietary cartridge adhesive to the underside of the profile, then, ensuring the substrate is free from dust, firmly place the base into position.  *On timber subfloors, apply adhesive, and fix using No6 wood screws.

- Secure in place using a No6 fixing screw.

- Once secured, install the carpet into the profile (it is recommended that the carpet is sealed to avoid any fraying).  Using a rubber mallet and timber baton firmly strike the top of the section so it flattens into the carpet pile.  Continue this process along the profile length until the whole of the top section sits flat.

- If any further information is required, please do not hesitate to contact Gradus Technical Services on (+44)1625 428922 or fax on (+44)1625 425226

Data Sheet:   (sheet 1 of 1)   23/04/12

# Accessories

Installation Guidelines

Gradus Accessories, Park Green, Macclesfield, Cheshire SK11 7LZ England UK  Tel: 01625 428922  Fax: 01625 433949

www.gradusworld.com

TH382 Threshold Trim