# Text boxes

# Accessories

Installation Guidelines

TH495 - Feature Strip

Data Sheet:  (sheet 1 of 1)   October 2014 DT

These installation guidelines apply to the following Gradus profile:

- It should be ensured that all surfaces to which the profiles are to be fixed are dry, flat and free from any contaminants prior to installation.

- Cut the profile to the length required.

- Mark the subfloor where the profile is to be fixed to aid where to place the adhesive.

- Apply a proprietary cartridge adhesive to the underside of the profile and to the marked area on the subfloor.

- Allow the adhesive to touch dry.

- Position the profile into position and then press firmly downwards to ensure good contact with the subfloor.

- Care should be taken when fitting floorcoverings into the cover areas of the profile.

Recommended adhesive products for traditional threshold trims.

Gradus Limited provides this information only as guidance and the legal responsibility for the supply and performance of the adhesives listed below shall remain the sole responsibility of the relevant manufacturer.

By providing this information, Gradus Limited does not imply any equivalents between each of the different manufacturers’ products, or that other products would prove unsatisfactory.  However, use of adhesives not recommended by Gradus should be supported by a guarantee from the adhesive supplier.

Application of the named adhesive must be actioned in strict accordance with the relevant manufacturers’ instructions.

If you have any queries regarding adhesives, please contact the adhesive manufacturer directly.

| Manufacturer | Product Reference | Contact number | Website |
| --- | --- | --- | --- |
| F. Ball and Co. Ltd | F32 / F33 | +44 (0) 1538 361 633 | http://www.f-ball.co.uk/ |
| Tremco | SP060 / MT440 | +44 (0) 1942 251400 | http://www.tremco-illbruck.co.uk/ |
| UZIN | MS Structural | +44 (0) 1788 530 080 | http://www.uzin.co.uk/ |

Gradus Accessories, Park Green, Macclesfield, Cheshire SK11 7LZ England UK Tel: 01625 428922 Fax: 01625 433949

www.gradusworld.com

09/13/DT